The files in this directory refer to basic experiments on LTP. They have been obtained with tcpdump on the interface of vm1 to vm2.

Syntax: tcpdump -i ens4 -w nameOfFile &
i=interface
w=write on nameOfFile
& run in background
fg (foreground) at the end of experiment, and then ctrl+c.

They should be analyzed with Wireshark.

1) LTP_nolosses
1 bundle of 50 kB is sent via LTP from vm1 to vm2. The bundle is encapsulated in an LTP block; the LTP block is divided into segments (1022 B each); each segment is sent in a UDP packet.
The last segment is flagged as a checkpoint (CP) and its arrival at vm2 triggers a report segment (RS) with one claim, confirming all data received. At its reception the RS is confirmed, as always by an RS ack.

2)LTP_PER4
The same as before, but with a PER=4% on the channel. This time a few “pure” data segment (not flagged as CP) are lost, therefore the first RS does not confirm all data. Data received (bytes) are specified by 5 “claims”. All other data are considered lost, and corresponding LTP segments are retransmitted immediately after the RS-ack (5 re-Tx segments), the last of which is flagged as CP. This CP triggers a second RS, informing vm1 that this time all data have been received.
In brief, it is the same as before, but one re-tx cycle.

3) LTP_PER10_4_ReTx_Cycles
As before, but with a PER=10%. This time we have 4 retransmission cycles because we have losses on retransmitted segments, due to the higher PER.

4) LTP_PER10_CPlost
This time the CP at row 50 is not followed by an RS, but is retransmitted after 2.5 s (one RTO), see row 51. After that we have one cycle of retransmission. This example shows that the lost of a CP requires an additional RTO, thus is worse than the lost of a “pure” data segment.